## Slide 1
Douglas Forsyth
Executive Director for Facilities and Strategic Planning
and
Chief, Radar Research & Development Division
Looking to the Future
Radar Research
Presentation For
The Kimpel Symposium
June 2010

## Slide 2: NSSL RADAR HISTORY
1960s
2000
WSR-57
Research
1970
1980
1990
1971
Norman
10cm
Doppler
1971
Cimarron
10cm
Doppler
1973
1973
1974
First Dual
Doppler
Analysis
1974
JDOP
77-79
Initial Algorithm Development
Mesocyclone
Wind Profiling
81-86
1984
Cimarron Upgraded
Dual-Polarization
83-84
First Dual-polarization Time Series
1984
First WSR-88D
Installed
1989
First Dual-polarization Real Time
Displays
1992
First PPP for NOAA P-3
1980
First Dual Doppler using P3 & Cimarrron
1989
First Calculations of
Differential Phase &
Cross Correlation Coefficient
Helped build First DOWs
1995
First WSR-88D Research Radar
1996
WDSS

## Slide 3: NSSL RADAR HISTORY
2000
2009
NWRT
Operational
Dual Polarization
2001
2003
2005
2007
2002
2006
2004
2008
1st Tornado
With PAR
ORPG
OPUP
ORDA
RRDA
WDSS-II
1st PAR data
Initialize Model
)

## Slide 4: What’s in the near Future
Fleet of Dual Polarized S-Band Radars
Real-time initialization of Storm Scale Models
Real-time 4-D virtual radar data bases
Access and combining of various types of radar systems (different freq, different resolutions, etc)
Decrease in Volumetric data collection times (Faster Volume Scans)
Improved understanding of thunderstorm evolution as seen by radar

## Slide 5
Polarimetric Tornado Detection
Oklahoma City tornado on 8 May 2003
Tornadic debris has distinct polarimetric signature

## Slide 6
Polarimetric Signatures in Supercell Storms
Recent investigations (Ryzhkov et al. 2005; Kumjian and Ryzhkov 2008,2009) have revealed repetitive polarimetric radar signatures in supercell storms. These signatures are unique to supercells and provide insight into the storm’s evolution and behavior and exemplify links between storm kinematics and microphysics.
One such signature is the low-level ZDR “arc”

## Slide 7: Wind retrieval on conical surface NWRT 20070509
81x81pts
500mX500m
Moving Frame U=2m/s
V=11m/s
Phase Array radar
Courtesy of Qin Xu

## Slide 8
8
New Adaptive Scanning Capability
Notes: 2008 AMS Conference
8

## Slide 9: ADAPTS Performance Qualitative Evaluation
ADAPTS is OFF
ADAPTS is ON
09 AUG 2008 – Reflectivity - 8.7 deg

## Slide 10: ADAPTS Performance Quantitative Evaluation
10
0040:59
0104:35
0129:24
0154:27
0217:27
Time (UTC)
Temporal Resolution (min)
0.9
1.0
1.1
1.2
1.3
1.4
a)
0040:59
0129:24
0217:27
b)
200 km
150 km
100 km
200 km
150 km
100 km
200 km
150 km
100 km
1 May 2009
Nominal Update Time
ADAPTS Update Times
Time Savings

## Slide 11: Range Oversampling

## Slide 13
223346 UTC
PAR Reflectivity cross-section, cappi (10 km), and 0.5 PPI
Images ~ 26 s
Earlier detection of large hail aloft
15 August 2006
Simulated WSR-88D Reflectivity cross-section, cappi (10 km), and 0.5 PPI
Images ~ 5 min

## Slide 14
223346 UTC
PAR Reflectivity & Velocity 0.5 PPI
Images ~ 58 s
Earlier detection of velocity signatures
24 April 2006
KTLX Reflectivity & Velocity 0.5 PPI
Images ~ 4 min

## Slide 15
PAR VCP 12 BMX 60 sector
0.5 oversampling in azimuth
Images ~ 43 s
WSR-88D VCP 12 Images ~ 4.1 min
Tropical Storm Erin: Eyewall
PAR
KTLX
PAR
KTLX
19 August 2007

## Slide 16: 5-10 years
Development of Cost affordable Dual-Polarized Phased Array
Multi-function Phased Arrays
Automated Adaptive Scanning
4-D User Interface between data and Users
Real-time delivery of radar data and warnings to hand-held portable devices, automobiles, airplanes, etc.

## Slide 17
Potential uses of Phased Array Radar

## Slide 18: FAA/BCI Aircraft Tracking

## Slide 19: ASR-9 vs. ATP / May 21, 2009 16:27:28 – 16:32:28 GMT
Courtesy of Basic Commerce Industries
ASR-9
ATP

## Slide 20: Multi- Receiver System
eight LNA’s
eight downconverters
Installed rack w/ digital receivers
1 - Az Diff
1 - El Diff
6 – Clutter Channels
Monopulse
Courtesy of Mark Yeary

## Slide 21: Signature of Airplane

## Slide 22: Example of Release

## Slide 23: User Interface – Adaptive Scanning

## Slide 24: 3D Isosurface Display
Animation of reflectivity core
(green) and mesocyclone
vortex (purple)

## Slide 25: 10-20 years
No Crystal Ball, but
  Technology is still expanding at an exponential rate (faster and smaller)
  Some think that computers will exceed the capacity of the human brain
  Systems will be robotic
  Weather radars (conformal phased arrays) will be available on various mobile vehicles and will uplink information for mutual use
  Warn-on-forecast will be a reality

## Slide 26: Warn on Forecast

## Slide 27: Questions?
Questions:
THANK YOU