## Slide 1: Multi-Radar Multi-Sensor (MRMS) – Flooded Locations and Simulated Hydrographs (FLASH)
Jonathan J. Gourley
February 25–27, 2015
National Weather Center
Norman, Oklahoma

## Slide 2
Multi-Radar Multi-Sensor QPE (MRMS)
Flooded Locations And Simulated Hydrographs (FLASH)
- An NWS CONUS-wide flash-flood forecasting system
MRMS/Q3 Rainfall Observations
1km2/2 min
Stormscale Distributed Hydrologic Model Ensemble
-1km2/10 min
10-11 June 2010, Albert Pike Rec Area, Arkansas
250 mm
200
150
20 fatalities
Hydro-FACETs
Simulated surface water flows and return period
Probabilistic Forecast Products on the Flash Flood Impacts and Magnitudes (70% chance of hazardous road flooding)
Indicator of Relevance
NSSL’s Grand Scientific Challenge #3:
Reliably predict flash flooding for both urban and complex landscapes out to several hours

## Slide 3: Ensemble Framework for Flash Flood Forecasting
SAC
Coupled Routing and Excess Storage (CREST; Wang et al. 2011)
Kinematic Wave
Routing
0.01 mm/h
51 mm/h
All Parameters from Basin Properties
KSat
Figure adapted from UC-Irvine
3
Notes: Wang, J., Y. Hong, L. Li, J. J. Gourley, S. I. Khan, K. K. Yilmaz, R. F. Adler, F. S. Policelli, S. Habib, D. Irwin, A. S. Limaye, T. Korme, and L. Okello, 2011: The coupled routing and excess storage (CREST) distributed hydrological model. Hydrol. Sci. Journal, 56, 84-98, doi: 10.1080/02626667.2010.543087

## Slide 4
Estimates (via regression) at gauged locations
Channel routing parameters at USGS stream gauges

## Slide 5
Extended to all grid points using statistical model (Rigby and Stasinopoulos, 2005)
Significant explanatory variables: 1. Annual Precip, Mean Temp, Relief Ratio, Basin Area
Notes: *Rigby, R.A. and D.M. Stasinopoulos, 2005: Generalized additive models for location, scale and shape. Appl Stat-J Roy St C, 54, 507–554.

## Slide 6
Real-time, direct simulation of flash floods a reality (flash.ou.edu)
0-6 hr streamflow, average recurrence intervals, and soil moisture forecasts…
everywhere
6

## Slide 7: Subjective and Quantitative Evaluations
2002-2011 using MRMS precip reanalysis (1 km/5min)
CREST model (uncalibrated)
256 gauged basins
Evaluate simulation of event peakflow
All USGS gauges
Catchments < 260 km2
1. HWT-Hydro Testbed Experiment
2. US Flash flood observation data base (Gourley et al., 2013, BAMS)
Notes: Gourley, J. J., Y. Hong, Z. L. Flamig, A. Arthur, R. A. Clark, M. Calianno, I. Ruin, T. Ortel, M. E. Wieczorek, E. Clark, P.-E. Kirstetter, and W. F. Krajewski, 2013: A unified flash flood database across the United States, Bull. Amer. Meteor. Soc., 94, 799-805. doi: http://dx.doi.org/10.1175/BAMS-D-12-00198.1

## Slide 8: Event-Based Evaluation (Peakflow)
Quantiles describing observed vs. simulated peakflows using error model (Rigby and Stasinopoulos, 2005)
Future work will extend/regionalize error model to specific hydroclimatic, geomorphologic regimes
q50
q75
q95
q25
q5
N=1932
Notes: *Rigby, R.A. and D.M. Stasinopoulos, 2005: Generalized additive models for location, scale and shape. Appl Stat-J Roy St C, 54, 507–554.

## Slide 9: Multi-radar Multi-sensor (MRMS) Operational Implementation Schedule to NWS/NCEP
MRMS-Severe
QPE
Flash Flood
MRMS-Aviation
MRMS-Hydro
10/15
CREST# (Streamflow, ARI, Soil Moisture)
04/16
Sacramento (Streamflow, ARI, Soil Moisture)
Probabilistic QPE+
04/17
QPF inputs to FFG, ARI, hydro models
Probability of Flash Flood
Probability of Debris Flow
Impact-Specific Products
#CREST = Coupled Routing and Excess Storage model (Wang et al., 2011)
*Rainfall ARIs computed by comparing real-time MRMS QPE to NOAA Atlas 14 precipitation frequency estimates
07/15
QPE-to-Flash Flood Guidance (FFG) Ratio
QPE Average Recurrence Interval (ARI*)
+PRORATE=Probabilistic QPE using Radar Observations of Rate And Typology Estimates (Kirstetter et al., 2015)
9
Notes: Wang, J., Y. Hong, L. Li, J. J. Gourley, S. I. Khan, K. K. Yilmaz, R. F. Adler, F. S. Policelli, S. Habib, D. Irwin, A. S. Limaye, T. Korme, and L. Okello, 2011: The coupled routing and excess storage (CREST) distributed hydrological model. Hydrol. Sci. Journal, 56, 84-98, doi: 10.1080/02626667.2010.543087
Kirstetter, P. E., J. J. Gourley, Y. Hong, J. Zhang, S. Moazamigoodarzi, C. Langston, and A. Arthur, 2015: Probabilistic precipitation rate estimates with ground-based radar networks. Wat. Resour. Res. (in press).

## Slide 10: Summary
53 peer-reviewed articles on remote sensing of precipitation and flood forecasting in past 5 years
$1.4 million of project funding brought in from NOAA, NASA, and NSF (weighted by SRI%) in past 5 years
Guest editor for J. Hydrol. special issue on Flash floods, hydro-geomorphic response and risk management, 2014-present
AMS J. Hydrometeor. Editor’s Award, 2013
NASA Goddard Space Flight Center Robert H. Goddard Award (Team) for the category of Exceptional Achievement in Science, 2015
Dept. of Commerce Bronze Medal Award, 2012
Member of NASA’s Precipitation Measurement Mission Science Team, 2013-present
Member of AGU’s Precipitation Technical Committee, 2010-present