## Slide 1: Multi-Function Phased Array Radar (MPAR)
Kurt D. Hondl (NOAA/NSSL)
February 25–27, 2015
National Weather Center
Norman, Oklahoma

## Slide 2: Q) Why Phased Array Radar?
To meet NOAA’s evolving requirements
for radar observations.
Faster Volume Updates
  Improved Probability of Detection (POD) and False Alarm Ratio (FAR), increased tornado warning lead-times
  Data assimilation into numerical weather models (Warn On Forecast)
Electronic Adaptive Scanning
  Based on prioritization – Scan when and where needed
These benefits are not possible with the WSR-88D

## Slide 3: Electronic Scanning
Conventional scanning
Sequential scanning only
(including “clear” air)
NEXRAD
Electronic Adaptive scanning
Concentrates radar
only on areas of concern
Phased Array Radar
http://wdssii.nssl.noaa.gov/web/wdss2/products/radar/MPAR/par_scan.shtml
Notes:   Faster scans by concentrating on areas of interest
  Potentially better data (due to non-moving antenna so no smearing)
  Faster re-visit times for selected targets (aircraft or tornadoes)
  Different scans for aircraft vs weather vs biological targets

## Slide 4: El Reno EF3 Tornado 31 May 2013
NWRT/PAR: 1.2-min updates
WSR-88D: 4.2-min updates
Transition to tornadic storm seen earlier and more clearly by Phased Array Radar
Direction of tornado path captured better by Phased Array Radar
http://wdssii.nssl.noaa.gov/web/wdss2/products/radar/MPAR/NWRT/ELReno_NWRTPAR.gif

## Slide 5: MPAR Concept
Weather
Radar
Aircraft
Radar
Mechanically Rotating
Electronically Steered
Consolidated Maintenance, Logistic and Training Programs
Multiple Maintenance, Logistic and Training Programs
Scalable to Mission Needs
Non-Scalable
Multi-Mission
Single Mission
Single System
Eight System Types
Legacy & Emerging Requirements
Legacy Requirements
ARSR-4
FPS
CARSR-1/2/3
ASR-8
ASR-9
ASR-11
TDWR
WSR-88D

## Slide 6: NSWRC and MPAR
Federal Enterprise MPAR Deployment
DoD/DHS Participation Accommodated
Adds Replacement of CARSR/ARSR-4/FPS (122 radars)
FAA NOAA Collaboration
NOAA providing funding and in-kind support
Adds NWS WSR-88D replacement (156 radars)
FAA NSWRC
NextGen Surveillance & Weather Radar Capability
Program of Record
Replaces ASRs and TDWR (276 radars)
Engaged in MPAR risk reduction
Other options are being considered
Potential savings of $1.8B in acquisition costs by reducing the total number of radars from 554 to ~365
(2006 Office of the Federal Coordinator for Meteorology report)

## Slide 7: MPAR R&D Focus Areas
Acceptable Cost
  Exploit Commercial Technology
  Fewer Systems Overall
  Economies of Scale
  Graceful Degradation
  Single Logistics & Maintenance System
Multi-Functionality
  Resource Management
  One System that Meets Multiple Needs
  Data Sharing and Operational Flexibility
Dual Polarization Capability
  Unique Weather Requirement of WSR-88D
  Improved Clutter Rejection & Aircraft Detection

## Slide 8: Differential Reflectivity
Larger rain drops are oblate
Smaller rain drops are more spherical
ZH needs to be parallel to the earth at all viewing angles to effectively capture the aspect ratio of the rain drop.
Smaller drops -- Diameter ~ 0.5 mm
Larger drops -- Diameter ~ 4.0 mm
Notes: WSR-88D recently upgraded to send out horizontal and vertical polarizations.
Use the difference in horizontal and vertical returns signals to provide info on particle size/shape
Need to be able to measure that very small difference

## Slide 9: Electronic Scanning
Phased Array Antenna
Phased Array Antenna
Broadside beam
(beam is perpendicular to the array face)
EV and EH are orthogonal
Off-Broadside beam
(beam is not perpendicular to the array face)
EV and EH are skewed
1.5°
2.1°
EV
EH
EV
EH
Beam is circular in shape and H is parallel to the surface of the earth
Beam is elliptical in shape and H is not parallel to the surface of the earth

## Slide 10: MPAR Activities
Industry Activities
Technology Development Activities
NOAA/FAA
Activities
National Weather Radar Testbed / Phased Array Radar (2003-2014)
  Meteorological phenomena studies, Adaptive scanning, Warning decision-making process, Multi-function demonstration
MPAR-Sponsored Studies (2010-2014)
  Siting study, Spectrum analysis, Preliminary cost study, Microburst / Windshear assessment, Backend analysis
Industry Engagement
  Request for Information (2012)
  Industry Day (2012)
Sponsored Industry Studies
  Phased Array Radar Dual Polarization Engineering Approaches (2012)
  Antenna Design and Life Cycle Cost Estimation (2013)
Cylindrical Polarized Phased Array Radar (2011-2105)
  OU/ARRC proof of concept demonstrator, CPPAR Design study
10-Panel Dual Polarization Demonstrator Development (2012-2015)
  MIT/LL Gen 2+ panel technology, OU transceivers, Final assembly in progress
Advanced Technology Demonstrator (ATD) Design (2014-2015)
  Preparing for evaluation prior to FAA/NSWRC Initial Investment Decision (IID)

## Slide 11: Cylindrical Polarized PAR (CPPAR)
Developed by OU Advanced Radar Research Center (ARRC)
CPPAR Objectives
  Demonstrate properties of cylindrical arrays
    Scan strategies
    Dual polarization performance
    Calibration concept
  Gain understanding of cylindrical array benefits and limitations
  Joint NSSL & ARRC full-scale CPPAR design study 2013-2014
    Included all-digital radar architecture
Initiated all-digital array design (fall 2014)

## Slide 12: 10-Panel Dual Pol Demonstrator
Developed by MIT/Lincoln Laboratory
Dual Polarization Panels
  Successive generations of design starting in 2007
    Previous funding provided by FAA, and USAF. Demonstrator funded by NOAA.
10-Panel Demonstrator Objectives
  Demonstrate sufficient progress towards identified risk areas
    Dual polarization performance
    Calibration concept
    Thermal management
  Testing at NSSL during spring 2015
    Evaluation for FAA Investment Analysis Readiness Decision (IARD, Dec 2015)
    Is the MPAR concept mature enough to be included in the analysis of alternatives?

## Slide 13: Dual Polarization Evaluation
Light rain: Zdr at vertical incidence
Radar should see near 0 Zdr values at all pointing angles. Retest after rotation azimuth ±90-deg
Z
X
Vertical Scan

## Slide 14: Dual Polarization Evaluation
Self Consistency Check
Successive scans of the same storm at different angles will allow an inter-comparison to validate polarization calibration and correction procedures
Area sampled by 5 different scanning angles
Y
X
Horizontal Scan

## Slide 15: Advanced Technology Demonstrator
SPY-1A Antenna
Antenna Position Programmer
1970’s Technology
NWRT/ATD
NWRT/PAR
Plan to build a new phased array radar with mature, available components
MIT/LL dual polarization panel technology
DOD-developed receivers, exciters, and beamformers
Using a combination of NSSL-developed and DOD-developed software
To demonstrate MPAR-like technology prior to FAA Initial Investment Decision
Will have capabilities that cannot be demonstrated on the NWRT/PAR
NOAA and FAA sharing development costs of ATD
A Modern, Active Array, Dual Polarization, Phased Array Radar

## Slide 16: FAA NSWRC Timeline
2010 2011 2012 2013 2014 2015 2016 2017 2018 2019
Mission Analysis Investment Analysis
Service Gap Analysis Concepts & Req Def Initial IA Final IA
CRDR IARD IID FID
Preliminary Requirements
Analysis of Alternatives
Cost/Benefit Estimate
Update Requirements
Select Preferred Alternative
Define Business Case
Finalize Requirements
Solicit/ Evaluate Offers
Finalize Business Case
IARD FID ISD
2010 2015 2020 2025 2030 2035 2040 2045
MA IA Solution Implementation
In-Service Management
FAA Milestones
CRDR Concepts Requirements Definition
Readiness
IARD Investment Analysis Readiness
Decision
IID Initial Investment Decision
FID Final Investment Decision
ISD In Service Decision

## Slide 17: FAA NSWRC Timeline
IARD FID ISD
2010 2015 2020 2025 2030 2035 2040 2045
MA IA Prototype Implementation / Deployment
In-Service Management
2010 2015 2020 2025 2030 2035 2040 2045
MPAR Research
ATD
Pathfinding
NOAA Timeline
IID
WSR-88D SLEP
SLEP = Service Life Extension Program
Must be done to keep WSR-88D viable through 2030
Another SLEP?
Option A
Prototype
MPAR Deployment?
Deploy FAA radars first
Deploy NWS radars
starting ~2030
Option B

## Slide 18: MPAR Summary
Phased array radar technology may be necessary to meet evolving NWS requirements
  Simultaneous multi-function (weather and aircraft) operation only viable via phased array radar
NWRT/PAR has been a very valuable tool for MPAR R&D
  The Advanced Technology Demonstrator (ATD) is needed to perform additional MPAR R&D
MPAR R&D partnership with FAA is very strong
  Working together to build the ATD
  ATD offers an opportunity to initiate closer collaboration with the air surveillance components of DOD and DHS
FAA Initial Investment Decision is rapidly approaching
  NOAA will have a decision to make in December 2017

## Slide 19: MPAR Collaborators
Mark Benner, Rodger Brown, Richard Doviak, Pam Heinselman, Michael Jain, Michael Shattuck, Arthur Witt, Vincent Wood, Allen Zahrai, Dusan Zrnic
Ric Adams, Katie Bowden, Don Burgess, Chris Curtis, Eddie Forren, Douglas Forsyth, Igor Ivic, Charles Kuster, Valery Melnikov,
Djordje Mirkovic, David Priegnitz, Mike Schmidt, Robin Tanamachi, John Thompson, Sebastian Torres, Daniel Wasielewski

## Slide 20: Thank You