## Slide 1: New Concepts in Utilization of Polarimetric Weather Radars
Alexander Ryzhkov (CIMMS)
February 25–27, 2015
National Weather Center
Norman, Oklahoma

## Slide 2: Dual-polarization basics
Polarimetric radar variables are sensitive to hydrometeor (1) size, (2) shape, (3) orientation, (4) density, and (5) water content
Differential reflectivity Zdr = Zh/Zv
Shape
Orientation
Phase composition
Zv
Zh
ice
water

## Slide 3
160 research-quality dual-polarization operational radars
Role of NSSL in the NEXRAD polarimetric upgrade
Basic system design and participation in validation of radar variables and products
Providing initial set of operational algorithms
Developing necessary modifications of polarimetric radar algorithms and creating the new ones
Polarimetric upgrade of NEXRAD radars

## Slide 4: Classification of different types of radar echo Hydrometeor Classification Algorithm (HCA)
Existing classes
GC/AP – ground clutter / AP
BS – biological scatterers
DS – dry aggregated snow
WS – wet snow
CR - crystals
GR – graupel
BD – “big drops”
RA – light and moderate rain
HR – heavy rain
HA – hail (possibly mixed with rain)
New classes to be added
FRZ – freezing rain
IP – ice pellets
SH - small hail (D < 2.5 cm)
LH – large hail (2.5 < D < 5.0 cm)
GH – giant hail (D > 5.0 cm)
TDS – tornado debris signature
Novel approaches
Combining radar and NWP models
Using new crowd-sourcing techniques (SHAVE and mPING) for HCA validation

## Slide 5: Novel polarimetric techniques for rainfall estimation Advantages of using specific attenuation A
Gauge rain totals
Lower sensitivity to the variability of drop size distributions
Immunity to radar miscalibration, partial beam blockage, attenuation and impact of wet radome
Ideal for networking and compositing of rainfall maps from different radars
The bias due to beam blockage is eliminated in the R(A) rain total map

## Slide 6: Networking polarimetric radars
6 hr rain total
Mosaic rainfall map exhibits discontinuity if the R(Z) relation is used
The use of R(A) produces seamless mosaic rainfall map
Discontinuity

## Slide 7: Identification of the polarimetric “fingerprints” of various microphysical processes using cloud models and radar observations
Microphysical processes
Size sorting
Evaporation
Coalescence
Breakup
Freezing / refreezing
Depositional growth of ice
Aggregation
Riming
A catalog of polarimetric fingerprints of individual microphysical processes has been created
The fingerprints help forecasters to interpret radar data
Cloud modelers can use fingerprints to improve microphysical parameterization and assimilation of radar data
Polarimetric radar observation operator for cloud models has been developed

## Slide 8: Example of polarimetric fingerprints
Z
ZDR
ρhv
melting
riming
size sorting
ZH ZDR ρhv
ZH ZDR ρhv
ZH ZDR ρhv

## Slide 9: Summary
Successes
  Polarimetric weather radar technology was brought to operations
  The algorithms for hydrometeor classification and rainfall estimation have been further refined using novel concepts
  The concept of “polarimetric fingerprints” has been introduced
Remaining challenges
  Utilization of dual-polarization radars for improvement of the performance of the NWP models is a next frontier of research