## Slide 1: Innovative Techniques to Improve Weather Observations
David Warde (CIMMS/OU)
February 25–27, 2015
National Weather Center
Norman, Oklahoma
Notes: Slide 1: Introduction

## Slide 2
Signal Processing
Waveform
Generation
Detection
Parameter
Extraction
Sampling
Hardware
Functions
Software
Functions
Adapted from Rich Ice (ROC) presentation at Baron Weather Radar Summit,
7-8 Jan. 2015
Clutter
Filtering
Notes: Slide 2: Signal Processing
First “Weather Radar Summit” hosted by BARON Services, Inc.
  ~1/3 NSSL Lab presenters
  ~1/3 Other NOAA
  Other than NOAA/Baron
Signal Processing defined (Slide adapted from Rich Ice/ROC at Weather Radar Summit)
Evolution of Digital Signal Processing
  NSSL lead activities
  R2O
Clutter Mitigation

## Slide 3
Waveform
Generation
Detection
Clutter
Filtering
Parameter
Extraction
Sampling
Signal Processing – Pre-Doppler (1960s – 1980s)
Mostly
Non-existent
Fixed Pulse
Analog
Receiver
Intensity
Display
Antenna
Rotation
Speed
Envelope
Detection
DVIP
Levels
Experiments
With
R-Meters
Hardware
Functions
MTI
Radar?
Manual
Censoring
Software
Functions
All Hardware!
Usually with Vacuum Tubes!
Electronically
Generated
Countours
Uniformly
Spaced Pulses
Clutter
Filtering
Adapted from Rich Ice (ROC) presentation at Baron Weather Radar Summit,
7-8 Jan. 2015
Notes: Slide 2: Signal Processing
First “Weather Radar Summit” hosted by BARON Services, Inc.
  ~1/3 NSSL Lab presenters
  ~1/3 Other NOAA
  Other than NOAA/Baron
Signal Processing defined (Slide adapted from Rich Ice/ROC at Weather Radar Summit)
Evolution of Digital Signal Processing
  NSSL lead activities
  R2O
Clutter Mitigation

## Slide 4
Waveform
Generation
Detection
Clutter
Filtering
Parameter
Extraction
Sampling
Fixed Pulse
Analog
Receiver
Intensity
Display
Envelope
Detection
Hardware
Functions
Software
Functions
Stable/Coherent
Transmit Phase
Signal Processing – Doppler (1990s)
Quadrature
Phase
Detection
Multiple
Pulse Widths
Selectable
Number of
Samples
Two-Pulse
Canceler
IIR Notch
Filters
Clutter
Maps
Covariance
Estimators
(Velocity,
Spectrum Width)
Noise
Measurement
SNR and
Strong Point
Censoring
RV Mitigation:
Dual Scans
Dual PRFs
Uniformly
Spaced Pulses
Clutter
Filtering
Adapted from Rich Ice (ROC) presentation at Baron Weather Radar Summit,
7-8 Jan. 2015
Notes: Slide 2: Signal Processing
First “Weather Radar Summit” hosted by BARON Services, Inc.
  ~1/3 NSSL Lab presenters
  ~1/3 Other NOAA
  Other than NOAA/Baron
Signal Processing defined (Slide adapted from Rich Ice/ROC at Weather Radar Summit)
Evolution of Digital Signal Processing
  NSSL lead activities
  R2O
Clutter Mitigation

## Slide 5
Waveform
Generation
Detection
Clutter
Filtering
Parameter
Extraction
Sampling
Hardware
Functions
Software
Functions
Signal Processing – Dual Polarization (2000s)
Uniformly
Spaced Pulses
Phase
Coded Pulses
Clutter
Filtering
Digital IF
Receiver
(14 bits)
Digital
Matched
Filter
“Indexed”
Radials
Selectable
Volume
Resolution
Adaptive
Spectral
Filter
Two-Pulse
Canceler
Clutter
Identification
Covariance
Estimators
(Dual Pol.
Parameters,
Hybrid SW)
Noise
Measurement
SNR and
Strong Point
Censoring
RV Mitigation:
Dual Scans
Dual PRFs
Phase Coding
Dual Polarization
Adapted from Rich Ice (ROC) presentation at Baron Weather Radar Summit,
7-8 Jan. 2015
Notes: Slide 2: Signal Processing
First “Weather Radar Summit” hosted by BARON Services, Inc.
  ~1/3 NSSL Lab presenters
  ~1/3 Other NOAA
  Other than NOAA/Baron
Signal Processing defined (Slide adapted from Rich Ice/ROC at Weather Radar Summit)
Evolution of Digital Signal Processing
  NSSL lead activities
  R2O
Clutter Mitigation

## Slide 6: Ground Clutter Mitigation using Dual Polarization
Ground Clutter obscures meteorological data
  All meteorological variables are affected
  Contamination characterized by
    Near zero Doppler velocity
    Very narrow spectrum width (i.e., small velocity distribution)
Ground Clutter Filters mitigate contamination
  May not remove all of the contaminant
  May remove some of the weather signal
    Near zero Doppler velocity
  Misapplication degrades data quality!
Notes: Slide 3: Ground Clutter/mitigation
Ground clutter
  Obscures weather data
  All meteorological variables affected
  Characteristics of ground clutter
Ground Clutter filter
  Mitigates ground clutter contamination
  Weather along zero-isodop
  Misapplication

## Slide 7: Snowing in Duluth, MN
Reflectivity
Differential Reflectivity
Correlation Coefficient
Velocity
21:25Z
Using WSR-88D Ground Clutter Mitigation
Notes: Slide 4: Duluth, MN (October 20, 2013)
Current ground clutter mitigation
  Dual Polarization based
  Detection and ground clutter filter separate algorithms
Operators see ground clutter signature
  correlation coefficient reduced values
  Some enhancement of differential reflectivity
  Not readily visible in reflectivity
  Not readily visible in velocity
Mitigate using all bins clutter filter to ~50 Km
  Zero-isodop loss in all estimates
Automate ground clutter mitigation (Give the operator the tools)

## Slide 8: Snowing in Duluth, MN
Reflectivity
Differential Reflectivity
Correlation Coefficient
Velocity
21:35Z
All Bins Clutter Filtering to ~50km
Notes: Slide 4: Duluth, MN (October 20, 2013)
Current ground clutter mitigation
  Dual Polarization based
  Detection and ground clutter filter separate algorithms
Operators see ground clutter signature
  correlation coefficient reduced values
  Some enhancement of differential reflectivity
  Not readily visible in reflectivity
  Not readily visible in velocity
Mitigate using all bins clutter filter to ~50 Km
  Zero-isodop loss in all estimates
Automate ground clutter mitigation (Give the operator the tools)

## Slide 9
Ground Clutter
Weather
No Weather/No Ground Clutter
Clutter Dominates
Weather Dominates
Mix Ground Clutter/Weather
Weather Environment Thresholding
(WET)
(Detects weather
dominate regions)
CLEAN-AP1
(Integrates ground clutter detection and filtering)
1CLEAN-AP © 2009 Board of Regents
of the University of Oklahoma
Notes: Slide 5: Venn diagram
Clutter
Weather
Mixed Clutter/Weather
  Clutter dominate
  Weather dominate
    Some weather estimates more sensitive to clutter contamination
CLEAN-AP/WET
  CLEAN-AP (Clutter environment analysis using adaptive processing)
    Integrates detection/filtering
    Developed at NSSL
    OU holds copyright/Government free license
    R2O
      Originally developed for NWRT PAR
      Adapted for WSR-88D dual polarization for Staggered PRT and Uniform waveforms
      Algorithm transferred to ROC
  WET (Weather environment thresholding)
    Detects weather dominate signals using dual polarization parameters
    Passes for further processing if non-weather
    Preserves best quality of weather dominate weather estimate
    Current research
    Presented at AMS 2015 annual meeting, Phoenix, AZ

## Slide 10: Once Again… Snowing in Duluth, MN
Reflectivity
Velocity
Spectrum Width
Differential Reflectivity
Correlation Coefficient
Differential Phase
Unfiltered
Notes: Slide 6: Duluth, MN (March xx, 2013)
Unfiltered (reflectivity, velocity, spectrum width, differential reflectivity, correlation coefficient, and differential phase)
WET/CLEAN-AP processed

## Slide 11: Once Again… Snowing in Duluth, MN
Reflectivity
Velocity
Spectrum Width
Differential Reflectivity
Correlation Coefficient
Differential Phase
Unfiltered
WET/CLEAN-AP
Notes: Slide 6: Duluth, MN (March xx, 2013)
Unfiltered (reflectivity, velocity, spectrum width, differential reflectivity, correlation coefficient, and differential phase)
WET/CLEAN-AP processed

## Slide 12: Summary of R2O Activities Transferring Innovative Techniques to the NEXRAD Network
Recent Transfers
Staggered pulse repetition time (PRT)
CLEAN-AP (uniform PRT and staggered PRT)
SZ-2 censoring
Polarimetric-variable-specific SNR thresholds
Less tapered window for super-resolution DP variables
Coherency-based thresholding
Noise estimator
Notes: Slide 7: R2O Acitivities (DSP)
Transferred
Ready
Research
Planned

## Slide 13: Summary of R2O Activities Transferring Innovative Techniques to the NEXRAD Network
Ready for Transfer
Improved spectrum width estimator
Improved correlation coefficient estimator
Range oversampling processing
Combining H&V autocovariance estimates for Doppler velocity estimates
Notes: Slide 7: R2O Acitivities (DSP)
Transferred
Ready
Research
Planned

## Slide 14: Summary of R2O Activities Transferring Innovative Techniques to the NEXRAD Network
Research in Progress
Combining autocovariance estimates from different scans for DP variables
Multi-lag estimators for DP variables
Using differential-phase information to improve the mitigation of ground clutter (WET)
Pulsed-interference filter
Notes: Slide 7: R2O Acitivities (DSP)
Transferred
Ready
Research
Planned

## Slide 15: Summary of R2O Activities Transferring Innovative Techniques to the NEXRAD Network
Planned Research
Wind turbine clutter mitigation
Spatial reconstruction of censored data
Ground clutter mitigation using spectral decomposition of DP variables
Artifacts removal and data quality improvement using range-Doppler spectrum
Notes: Slide 7: R2O Acitivities (DSP)
Transferred
Ready
Research
Planned